## Slide 1: Solar Spinner
Demonstrates the conversion of solar energy into electricity and then mechanical energy

## Slide 2
100 mm plastic petri dish
Solar cell (very brittle)
¼ “ adhesive conductive copper foil

## Slide 3
Corners of solar cell are clipped so it fits on bottom of smaller petri dish

## Slide 4
Back of solar cell with silver contact strips- collects positive charge
Position of copper tape

## Slide 5
Partially remove tape backing-
gently press on back contact starting 1” from edge
Solar cell must be flat on table

## Slide 6
Top of cell collects the negative charge
Copper strip covers the silver strip starting ½” from edge of the cell.
Don’t let the front and back contact strips touch = short circuit

## Slide 7
Wrap top contact over and around edge of petri dish

## Slide 8
Fold bottom strip over on itself so sticky side touches dish,
wrap around edge of petri dish

## Slide 9
Test the voltage of the cell on the 2 volt
range, to make sure it is connected
correctly- .3-.55 volts

## Slide 10
Place the petri dish cover and secure with 2 pieces of clear plastic tape.

## Slide 11
Thread thin copper wire through the lugs on the back of the motor
and bend over about ¼”

## Slide 12
Solder the copper wire to each lug.

## Slide 13
Hot glue two spacer strips to the back of the motor
And add a piece of foam tape to each.
Hot glue
Foam tape

## Slide 14
Solder motor wires to the copper strips coming from the solar cell.
Test the motor to see that it is turning in the light.

## Slide 15
Peel off backer on foam tape-
carefully center the motor on the dish, press down.

## Slide 16
Decorate your Solar Spinner

## Slide 17: Mount the spinner on a block of wood or stick with a hole drilled to fit the shaft. Put the solar spinner in your yard or sunny window. What other creations can you make with this as a starting point?

## Slide 18: Make more at your school
Amazon-
  Copper tape
  Petri dishes
  Copper wire
Ebay – solar cells $.50 each
Electronics Goldmine- high efficiency motor- $1.50
http://cei.washington.edu/education/lessons